Par-Kut International Standard Models
Partial Listing of Available Options

BULLET RESISTANT CONSTRUCTION: Booth construction to use material rated for U.L. 752 levels 1, 2, 3, 4, and 8.

CANOPY: Overhangs can range from None to 36”. Fascia can range from minimum required for devices, up to 25”. The 25” fascia is a split fascia used to conceal view of optional roof mounted air conditioner.

CASHIER CONVENIENCES: Slide-up, side sliding full height, or energy saving style cashier windows. Transaction drawers, deal trays, intercoms and ticket windows.

CASH MANAGEMENT: Locking cash drawers and drop safes.

CLEARANCE ISSUES: Removable lifting rings and custom heights for low clearance applications.

CLIMATE CONTROL: Through wall cool only or combination heat/cool type or roof mounted air conditioner units. Additional or higher watt output heaters. Package HVAC units.

CORROSION BARRIERS: Stainless steel base.

CUSTOM EXTERIORS: Two-color paint, Factory applied cast stone, stone aggregate panels, face brick, EIFS (Exterior insulation and finish system), ready-to-brick at site treatments and logos & vinyl signage.

DOORS: Top-suspended heavy duty sliding galvannealed steel, 18-gauge minimum, fully weather-stripped, with Adams Rite® #1850 hook bolt type lock, view window and all roller assembly hardware.  Trolleys shall be ball bearing, adjustable pendant type. Hinged steel door, with three ball bearing full mortise hinges with non-removable pins. Hinged door(s) shall include appropriately sized hydraulic closer (unless owner or code circumstances over-rule). Cylindrical type entrance lockset is standard.

ELECTRICAL: Load centers with higher amperage main disconnects and additional circuit breaker spaces. 3-Phase load centers, mini power-zones or transformers. Factory installed junction boxes and raceways for future field installed fire, security or communications equipment. Hazardous location lights, switches, heaters, air conditioner and outlets.

FLOORING: Vinyl composite floor tile, sheet vinyl or carpet mounted on ¾” exterior grade plywood sub floor; Lay in anti-fatigue mat (for buildings 4’ or 5’ wide only).

GLAZING: Tinted or Low-e or reflective or insulated safety glass or break resistant acrylic sheet or unbreakable polycarbonate.

INSULATION: Additional insulation in ceiling, floors and walls for severe weather areas.

LIGHTING: Recessed interior fluorescent lights, dimming incandescent down lights, fluorescent lighting under canopy overhang, single or duplex lamp exterior floodlights and traffic signal lights.

NOISE MANAGEMENT: Acoustical tile ceiling, sound deadening walls, laminated glass.

RECEPTACLES: Additional electrical outlets, isolated ground, surge suppression and ground fault interrupt receptacles.

SECURITY: Removable painted or galvanized security screens or welded burglar bars at all windows and doors.

VENTILATION: Exhaust fans (specify CFM) and louvers, ventilation windows with insect screen located per drawing.

WINDOWS: If operable windows are required, provide sliding windows as shown on drawings for ventilation and/or transaction purposes.  For ventilation windows, include insect screens.

WORK COUNTER: Plastic laminate or stainless steel upgrade or additional work counter.